## Slide 1: Advaned Computer Architecture: Basic Review
A Verilog Single-Cycle MIPS
Part I
Spring 2018
Reference: http://cadapplets.lafayette.edu/ece313/
Jeong-Gun Lee
Dept. of Computer Engineering, Hallym University
Jeonggun.lee@hallym.ac.kr
Notes: 1

## Slide 2: Outline
MIPS Instruction Set
  Registers and Memory 3
  MIPS Instructions
A Single-Cycle MIPS in Verilog
  Modeling basic datapath components
  Modeling the datapath
  Modeling the control unit
Notes: 4

## Slide 3: MIPS Registers and Memory
Memory
4GB Max
(Typically 64MB-1GB)
0x00000000
0x00000004
0x00000008
0x0000000C
0x00000010
0x00000014
0x00000018
0x0000001C
0xfffffff4
0xfffffffc
0xfffffffc
PC = 0x0000001C
Registers
32 General Purpose Registers
R0
R1
R2
R30
R31
32 bits

## Slide 4: MIPS Registers
Fast access to program data
Register R0/$0/$zero: hardwired to constant zero
Register names:
  $0-$31 or R0-R31
  Specialized names based on usage convention
    $zero ($0) - always zero
    $s0-$s7 ($16-$23) - “saved” registers
    $t0-$t7 ($8-$15) - “temporary” registers
    $sp - stack pointer
    Other special-purpose registers

## Slide 5: MIPS Registers and Usage

## Slide 6: More about MIPS Memory Organization
Two views of memory:
  232 bytes with addresses 0, 1, 2, …, 232-1
  230 4-byte words* with addresses 0, 4, 8, …, 232-4
Both views use byte addresses
Word address must be multiple of 4 (aligned)
8 bits
0x00000000
0x00000001
0x00000002
0x00000003
0x00000000
0x00000004
0x00000008
0x0000000C
32 bits
0
1
2
3
*Word sizes vary in other architectures
Not all architectures require this

## Slide 7: Outline - Instruction Sets
MIPS Instruction Set
  Registers and Memory
  MIPS Instructions 3
A Single-Cycle MIPS in Verilog
  Modeling basic datapath components
  Modeling the datapath
  Modeling the control unit
Notes: 4

## Slide 8: MIPS Instructions
All instructions exactly 32 bits wide
Different formats for different purposes
Similarities in formats ease implementation
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
I-Format
op
address
6 bits
26 bits
J-Format

## Slide 9: MIPS Instruction Types
Arithmetic & Logical - manipulate data in registers add $s1, $s2, $s3 $s1 = $s2 + $s3 or $s3, $s4, $s5 $s3 = $s4 OR $s5
Data Transfer - move register data to/from memory lw $s1, 100($s2) $s1 = Memory[$s2 + 100] sw $s1, 100($s2) Memory[$s2 + 100] = $s1
Branch - alter program flow beq $s1, $s2, 25 if ($s1==$s1) PC = PC + 4 + 4*25

## Slide 10: MIPS Arithmetic & Logical Instructions
Instruction usage (assembly) add dest, src1, src2 dest=src1 + src2 sub dest, src1, src2 dest=src1 - src2 and dest, src1, src2 dest=src1 AND src2
Instruction characteristics
  Always 3 operands: destination + 2 sources
  Operand order is fixed
  Operands are always general purpose registers
Design Principles:
  Design Principle 1: Simplicity favors regularity
  Design Principle 2: Smaller is faster

## Slide 11: Arithmetic Instruction Examples
C simple addition and assignment C code: A = B + C MIPS code: add $s0, $s1, $s2
Complex arithmetic assignment: C code: A = B + C + D; E = F - A; MIPS code: add $t0, $s1, $s2 add $s0, $t0, $s3 sub $s4, $s5, $s0
Compiler keeps track of mapping variables to registers (and, when necessary, memory)

## Slide 12: Arithmetic & Logical Instructions - Binary Representation
Used for arithmetic, logical, shift instructions
  op: Basic operation of the instruction (opcode)
  rs: first register source operand
  rt: second register source operand
  rd: register destination operand
  shamt: shift amount (more about this later)
  funct: function - specific type of operation
Also called “R-Format” or “R-Type” Instructions
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits

## Slide 13: Arithmetic & Logical Instructions - Binary Representation Example
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
Decimal
Binary
Machine language for add $8, $17, $18
See reference card for op, funct values
000000
0
10001
17
10010
18
01000
8
00000
0
100000
32

## Slide 14: MIPS Data Transfer Instructions
Transfer data between registers and memory
Instruction format (assembly) lw $dest, offset($addr) load word sw $src, offset($addr) store word
Uses:
  Accessing a variable in main memory
  Accessing an array element

## Slide 15: Example - Loading a Simple Variable
lw R5,8(R2)
Memory
0x00
Variable Z = 692310
Variable X
Variable Y
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
8
+
Registers
R0=0 (constant)
R1
R2=0x10
R30
R31
R3
R4
R5
R5
R2=0x10
R5 = 629310
Variable Z = 692310

## Slide 16: Data Transfer Example - Array Variable
Registers
R0=0 (constant)
R1
R2=0x08
R30
R31
R3
R4
R5=105
C Program: int a[5];
a[3] = z;
Assembly: sw $5,12($2)
12=0xc
+
Memory
0x00
a[0]
a[4]
a[2]
a[1]
a[3]
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
Base Address
R5=105
R2=0x08
a[3]=105
scaled offset

## Slide 17: Data Transfer Instructions - Binary Representation
Used for load, store instructions
  op: Basic operation of the instruction (opcode)
  rs: first register source operand
  rt: second register source operand
  offset: 16-bit signed address offset (-32,768 to +32,767)
Also called “I-Format” or “I-Type” instructions
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Address
source for sw
destination for lw

## Slide 18: I-Format vs. R-Format Instructions
Compare with R-Format
offset
6 bits
5 bits
5 bits
16 bits
I-Format
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
op
rs
rt
Note similarity!

## Slide 19: I-Format Example
Machine language for lw $9, 1200($8) == lw $t1, $1200($t0)
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Binary
Decimal
35
8
9
1200
100011
01000
01001
0000010010110000

## Slide 20: MIPS Conditional Branch Instructions
Conditional branches allow decision making beq R1, R2, LABEL if R1==R2 goto LABEL bne R3, R4, LABEL if R3!=R4 goto LABEL
Example C Code if (i==j) goto L1; f = g + h; L1: f = f - i; Assembly beq $s3, $s4, L1 add $s0, $s1, $s2 L1: sub $s0, $s0, $s3

## Slide 21: Example: Compiling C if-then-else
Example C Code if (i==j) f = g + h; else f = g - h; Assembly bne $s3, $s4, Else add $s0, $s1, $s2 j Exit; # new: unconditional jump Else: sub $s0, $s0, $s3 Exit:
New Instruction: Unconditional jump j LABEL # goto Label

## Slide 22: Binary Representation - Branch
Branch instructions use I-Format
offset is added to PC when branch is taken beq r0, r1, offset has the effect: if (r0==r1) pc = pc + 4 + (offset << 2) else pc = pc + 4;
Offset is specified in instruction words (why?)
What is the range of the branch target addresses?
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Conversion to
word offset

## Slide 23: Branch Example
Machine language for beq $s3, $s4, L1 add $s0, $s1, $s2 L1: sub $s0, $s0, $s3
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Binary
Decimal
4
19
20
1
000100
10011
10100
0000000000000001
$19
$20
PC
PC+4
Target
of beq
1-instruction
offset

## Slide 24: Comparisons - What about <, <=, >, >=?
bne, beq provide equality comparison
slt provides magnitude comparison slt $t0,$s3,$s4 # if $s3<$s4 $t0=1; # else $t0=0;
Combine with bne or beq to branch: slt $t0,$s3,$s4 # if (a<b) bne $t0,$zero, Less # goto Less;
Why not include a blt instruction in hardware?
  Supporting in hardware would lower performance
  Assembler provides this function if desired (by generating the two instructions)
condition register

## Slide 25: Binary Representation - Jump
Jump Instruction uses J-Format (op=2)
What happens during execution? PC = PC[31:28] : (IR[25:0] << 2)
op
address
6 bits
26 bits
Conversion to
word offset
Concatenate upper 4 bits
of PC to form complete
32-bit address

## Slide 26: Jump Example
Machine language for j L5
Assume L5 is at address 0x00400020
and
PC <= 0x03FFFFFF
Binary
Decimal/Hex
op
address
6 bits
26 bits
2
0x0100008
000010
00000100000000000000001000
>>2
lower 28
bits
0x0100008

## Slide 27: Constants / Immediate Instructions
Small constants are used quite frequently (50% of operands) e.g., A = A + 5; B = B + 1; C = C - 18;
MIPS Immediate Instructions (I-Format): addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4
Allows up to 16-bit constants
How do you load just a constant into a register?
ori $5, $zero, 666
Arithmetic instructions sign-extend immed.
Logical instructions don’t sign extend immed.

## Slide 28: Why are Immediates only 16 bits?
Because 16 bits fits neatly in a 32-bit instruction
Because most constants are small (i.e. < 16 bits)
Design Principle 4: Make the Common Case Fast

## Slide 29: MIPS Logical Instructions
and, andi - bitwise AND
or, ori - bitwise OR
Example
and $s2,$s0,$s1
ori $s3,$s2,252
11011111010110100100100011110101
11110000111100001111000011110000
$s0
$s1
$s2
11010000010100000100000011110000
$s3
11010000010100000100000011111100
00000000000000000000000011111100
(25210)

## Slide 30: Logical Operations - Applications
Masking - clear, set or test
  Individual bits
  Groups of bits

## Slide 31: Larger Constants
(original contents)
$t0
Immediate operations provide for 16-bit constants
What about when we need larger constants?
Use "load upper immediate - lui” (I-Format) lui $t0, 1010101010101010
Then use ori to fill in lower 16 bits: ori $t0, $t0, 1010101010101010
1010101010101010
0000000000000000
filled with zeros
$t0
1010101010101010
0000000000000000
1010101010101010

## Slide 32: MIPS Shift Instructions
MIPS Logical Shift Instructions
  Shift left: sll (shift-left logical) instruction
  Right shift: srl (shift-right logical) instruction
sll $s1,$s0,8
srl $s2,$s1,4
01011010010010001111010100000000
Zeros shift in
00000101101001001000111101010000
Zeros shift in
11011111010110100100100011110101
$s0
$s1
$s2

## Slide 33: Shift Instruction Encodings
Applications
  Bitfield access (see book)
  Multiplication / Division by power of 2
  Example: array access sll $t0,$t1,2 # $t0=$t1*4 add $t3,$t1,$t2 lw $t3, 0($t0)
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
srl
0
rs
rt
rd
0
shamt
sll
0
rs
rt
rd
6
shamt
unused

## Slide 34: Summary - MIPS Instruction Set
Three instruction formats
Similarities in formats ease implementation
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
I-Format
op
address
6 bits
26 bits
J-Format

## Slide 35: Advaned Computer Architecture: Basic Review with Verilog HDL
A Verilog Single-Cycle MIPS
Part 2
Spring 2018
Reference: http://cadapplets.lafayette.edu/ece313/
Jeong-Gun Lee
Dept. of Computer Engineering, Hallym University
Jeonggun.lee@hallym.ac.kr
Notes: 1

## Slide 36: Outline - A Single-Cycle MIPS in Verilog
MIPS Instruction Set
  Registers and Memory
  MIPS Instructions
A Single-Cycle MIPS in Verilog
  Modeling basic datapath components 3
  Modeling the datapath
  Modeling the control unit

## Slide 37: Single-Cycle Datapath Components
32-bit adder add32
32-bit ALU alu32
Parameterized 2-1 Multiplexer mux2
32-bit Simple Register reg32
32-bit Idealized Read/Write Memory mem32
32-bit MIPS-Style Register File reg_file
32-bit Idealized Read-Only Memory rom32
ALU Control Unit alu_ctl
Control Unit control_single

## Slide 38: 32-Bit Adder
// Behavioral model of a 32-bit adder
module add32(a, b, result);
input [31:0] a, b;
output [31:0] result;
assign result = a + b;
endmodule
Adder

## Slide 39: 32-Bit ALU
module alu(ctl, a, b, result, zero);
input [2:0] ctl;
input [31:0] a, b;
output [31:0] result;
output zero;
reg [31:0] result;
reg zero;
always @(a or b or ctl)
begin
case (ctl)
3'b000 : result = a & b; // AND
3'b001 : result = a | b; // OR
3'b010 : result = a + b; // ADD
3'b110 : result = a - b; // SUBTRACT
3'b111 : if (a < b) result = 32'd1;
else result = 32'd0; //SLT
default : result = 32'hxxxxxxxx;
endcase
if (result == 32'd0) zero = 1;
else zero = 0;
end
endmodule
ALU
zero

## Slide 40: 2-1 Multiplexer (Parameterized)
module mux2( sel, a, b, y );
parameter bitwidth=32;
input sel;
input [bitwidth-1:0] a, b;
output [bitwidth-1:0] y;
assign y = sel ? b : a;
endmodule

## Slide 41: 32-Bit Register (e.g., PC)
// Simple 32-bit register
module reg32 (clk, reset, d_in, d_out);
input clk, reset;
input [31:0] d_in;
output [31:0] d_out;
reg [31:0] d_out;
always @(posedge clk)
begin
if (reset) d_out <= 0;
else d_out <= d_in;
end
endmodule
32
32
CLK
reset
Data In
Data Out
REG

## Slide 42: Idealized Memory - Part 1
module mem32(clk, mem_read, mem_write, address, data_in, data_out);
input clk, mem_read, mem_write;
input [31:0] address, data_in;
output [31:0] data_out;
reg [31:0] data_out;
parameter BASE_ADDRESS = 25'd0;
reg [31:0] mem_array [0:31];
wire [4:0] mem_offset;
wire address_select;
assign mem_offset = address[6:2]
// address decoding
assign address_select = (address[31:7] == BASE_ADDRESS);

## Slide 43: Idealized Memory - Part 2
// for READ operations
always @(mem_read or address_select or mem_offset or mem_array[mem_offset])
begin
if (mem_read == 1'b1 && address_select == 1'b1)
begin
if ((address % 4) != 0)
$display($time, " rom32 error: unaligned address %d", address);
data_out = mem_array[mem_offset];
$display($time, " reading data: Mem[%h] => %h", address, data_out);
end
else // 메모리의 주어진 범위를 넘어설 때
data_out = 32'hxxxxxxxx;
end

## Slide 44: Idealized Memory - Part 3
// for WRITE operations
always @(posedge clk)
begin
if (mem_write == 1'b1 && address_select == 1'b1)
begin
$display($time, " writing data: Mem[%h] <= %h", address,data_in);
mem_array[mem_offset] <= data_in;
end
end
// initialize with some arbitrary values
integer i;
initial begin
for (i=0; i<7; i=i+1) mem_array[i] = i;
end
endmodule

## Slide 45: Register File
module reg_file(clk, RegWrite, RN1, RN2, WN, RD1, RD2, WD);
input clk;
input RegWrite;
input [4:0] RN1, RN2, WN;
input [31:0] WD;
output [31:0] RD1, RD2;
reg [31:0] RD1, RD2;
reg [31:0] file_array [31:1];

## Slide 46: Register File - Part 2
always @(RN1 or file_array[RN1])
begin
if (RN1 == 0) RD1 = 32'd0;
else RD1 = file_array[RN1];
$display($time, " reg_file[%d] => %d (Port 1)", RN1, RD1);
end
always @(RN2 or file_array[RN2])
begin
if (RN2 == 0) RD2 = 32'd0;
else RD2 = file_array[RN2];
$display($time, " reg_file[%d] => %d (Port 2)", RN2, RD2);
end
always @(posedge clk)
if (RegWrite && (WN != 0))
begin
file_array[WN] <= WD;
$display($time, " reg_file[%d] <= %d (Write)", WN, WD);
end
endmodule

## Slide 47: 32-Bit Idealized ROM
Input: 32-bit address
Output: 32-bit data
Use to model instruction memory

## Slide 48: 32-bit Idealized ROM - Part 1
// A simple 32-bit by 32-word read-only memory model
module rom32(address, data_out);
input [31:0] address;
output [31:0] data_out;
reg [31:0] data_out;
// address that applies to this memory
parameter BASE_ADDRESS = 25'd0;
reg [31:0] mem_arrray [0:31];
wire [4:0] mem_offset;
wire address_select;
// to get word offset
assign mem_offset = address[6:2];
// address decoding
assign address_select = (address[31:7] == BASE_ADDRESS);

## Slide 49: 32-bit Idealized ROM - Part 2
always @(address_select or mem_offset)
begin
if ((address % 4) != 0)
$display($time, " rom32 error: unaligned address %d", address);
if (address_select == 1)
begin
  case (mem_offset)
  5'd0 : data_out = { 6'd35, 5'd0, 5'd2, 16'd4 }; // 32bit
  5'd1 : data_out = { 6'd35, 5'd0, 5'd3, 16'd8 };
  5'd2 : data_out = { 6'd35, 5'd0, 5'd4, 16'd20 };
  5'd3 : data_out = { 6'd0, 5'd0, 5'd0, 5'd5, 5'd0, 6'd32 };
  5'd4 : data_out = { 6'd0, 5'd5, 5'd2, 5'd5, 5'd0, 6'd32 };
  5'd5 : data_out = { 6'd0, 5'd4, 5'd5, 5'd6, 5'd0, 6'd42 };
  5'd6 : data_out = { 6'd4, 5'd6, 5'd0, -16'd3 };
  5'd7 : data_out = { 6'd43, 5'd0, 5'd5, 16'd0 };
  default data_out = 32'hxxxx;
  endcase
$display($time, " reading data: rom32[%h] => %h", address, data_out);
end
end
endmodule

## Slide 50: 32-bit Idealized ROM - case
  case (mem_offset)
  5'd0 : data_out = { 6'd35, 5'd0, 5'd2, 16'd4 };
  // lw $2, 4($0) r2=1
  5'd1 : data_out = { 6'd35, 5'd0, 5'd3, 16'd8 };
  // lw $3, 8($0) r3=2
  5'd2 : data_out = { 6'd35, 5'd0, 5'd4, 16'd20 };
  // lw $4, 20($0) r4=5
  5'd3 : data_out = { 6'd0, 5'd0, 5'd0, 5'd5, 5'd0, 6'd32 };
  // add $5, $0, $0 r5=0
  5'd4 : data_out = { 6'd0, 5'd5, 5'd2, 5'd5, 5'd0, 6'd32 };
  // add $5, $5, $1 r5 = r5 + 1
  5'd5 : data_out = { 6'd0, 5'd4, 5'd5, 5'd6, 5'd0, 6'd42 };
  // slt $6, $4, $5 is r5 >= 5?
  5'd6 : data_out = { 6'd4, 5'd6, 5'd0, -16'd3 };
  // beq $6, $zero, -3 if not, go back 2
  5'd7 : data_out = { 6'd43, 5'd0, 5'd5, 16'd0 };
  // s2 $6, 0($zero) MEM[0] = $5
  // add more cases here as desired
  default data_out = 32'hxxxx;
  endcase

## Slide 51: ALU Control
Review - ALU Control Function
Operation
Desired Action
lw
add
sw
add
beq
subtract
add
add
sub
subtract
and
or
slt
and
or
set on less than
ALU Ctl.
010
010
110
010
110
000
001
111
funct
XXXXXX
XXXXXX
XXXXXX
100000
100010
100100
100101
101010
Instr. type
data transfer
data transfer
branch
r-type
r-type
r-type
r-type
r-type
ALUOp
00
00
01
10
10
10
10
10

## Slide 52: ALU Control Unit - Part 1
module alu_ctl(ALUOp, Funct, ALUOperation);
input [1:0] ALUOp;
input [5:0] Funct;
output [2:0] ALUOperation;
reg [2:0] ALUOperation;
// symbolic constants for instruction function code
parameter F_add = 6'd32;
parameter F_sub = 6'd34;
parameter F_and = 6'd36;
parameter F_or = 6'd37;
parameter F_slt = 6'd42;
// symbolic constants for ALU Operations
parameter ALU_add = 3'b010;
parameter ALU_sub = 3'b110;
parameter ALU_and = 3'b000;
parameter ALU_or = 3'b001;
parameter ALU_slt = 3'b111;
Symbolic Constants -
MIPS Function Codes
Symbolic Constants -
ALU Operations

## Slide 53: ALU Control Unit - Part 2
always @(ALUOp or Funct)
begin
case (ALUOp)
2'b00 : ALUOperation = ALU_add; // lw, sw
2'b01 : ALUOperation = ALU_sub; // beq
2'b10 : case (Funct)
F_add : ALUOperation = ALU_add;
F_sub : ALUOperation = ALU_sub;
F_and : ALUOperation = ALU_and;
F_or : ALUOperation = ALU_or;
F_slt : ALUOperation = ALU_slt;
default : ALUOperation = 3'bxxx;
endcase
default ALUOperation = 3'bxxx;
endcase
end
endmodule

## Slide 54: Main Control Unit
Review - Control Unit Function
Op5
Op4
Op3
Op2
Op1
Op0
RegDst
ALUSrc
MemtoReg
RegWrite
MemRead
MemWrite
Branch
ALUOp1
ALUOp0
0
0
0
0
0
0
1
0
0
0
1
1
1
0
1
0
1
1
0
0
0
1
0
0
1
0
0
1
0
0
0
1
0
0
1
1
1
1
0
0
0
0
X
1
X
0
0
1
0
0
0
X
0
X
0
0
0
1
0
1
OP
RT
lw
sw
beq
Input
Output

## Slide 55: Single-Cycle Control Unit - Part 1
module control_single(opcode, RegDst, ALUSrc, MemtoReg,
RegWrite, MemRead, MemWrite, Branch,
ALUOp);
input [5:0] opcode;
output RegDst, ALUSrc, MemtoReg, RegWrite, MemRead,
MemWrite, Branch;
output [1:0] ALUOp;
reg RegDst, ALUSrc, MemtoReg, RegWrite, MemRead,
MemWrite, Branch;
reg [1:0] ALUOp;
parameter R_FORMAT = 6'd0;
parameter LW = 6'd35;
parameter SW = 6'd43;
parameter BEQ = 6'd4;

## Slide 56: Single-Cycle Control Unit - Part 2
always @(opcode)
begin
case (opcode)
R_FORMAT :
begin
RegDst=1'b1; ALUSrc=1'b0; MemtoReg=1'b0;
RegWrite=1'b1; MemRead=1'b0; MemWrite=1'b0;
Branch=1'b0; ALUOp = 2'b10;
end
LW :
begin
RegDst=1'b0; ALUSrc=1'b1; MemtoReg=1'b1;
RegWrite=1'b1; MemRead=1'b1;
MemWrite=1'b0; Branch=1'b0; ALUOp = 2'b00;
end
SW :
begin
RegDst=1'bx; ALUSrc=1'b1; MemtoReg=1'bx;
RegWrite=1'b0; MemRead=1'b0; MemWrite=1'b1;
Branch=1'b0; ALUOp = 2'b00;
end

## Slide 57: Single-Cycle Control Unit - Part 3
case (opcode)
BEQ :
begin
RegDst=1'bx; ALUSrc=1'b0; MemtoReg=1'bx;
RegWrite=1'b0; MemRead=1'b0; MemWrite=1'b0;
Branch=1'b1; ALUOp = 2'b01;
end
default :
begin
$display("control_single unimplemented opcode %d",
opcode);
RegDst=1'bx; ALUSrc=1'bx; MemtoReg=1'bx;
RegWrite=1'bx; MemRead=1'bx; MemWrite=1'bx;
Branch=1'bx; ALUOp = 2'bxx;
end
endcase
end
endmodule

## Slide 58: Single-Cycle Processor - Wires

## Slide 62: Control Unit Design for Single-Cycle CPU
http://cis.k.hosei.ac.jp/~yamin/lectures/organization/sccu.html

## Slide 63: Single-Cycle Verilog - Part 1
module mips_single(clk, reset);
input clk, reset;
// instruction bus
wire [31:0] instr;
// break out important fields from instruction
wire [5:0] opcode, funct;
wire [4:0] rs, rt, rd, shamt;
wire [15:0] immed;
wire [31:0] extend_immed, b_offset;
wire [25:0] jumpoffset;
assign opcode = instr[31:26];
assign rs = instr[25:21];
assign rt = instr[20:16];
assign rd = instr[15:11];
assign shamt = instr[10:6];
assign funct = instr[5:0];
assign immed = instr[15:0];
assign jumpoffset = instr[25:0];

## Slide 64: Single-Cycle Verilog - Part 2
// sign-extender
assign extend_immed = { {16{immed[15]}}, immed };
// branch offset shifter
assign b_offset = extend_immed << 2;
// datapath signals
wire [4:0] rfile_wn;
wire [31:0] rfile_rd1, rfile_rd2, rfile_wd, alu_b, alu_out,
b_tgt, pc_next, pc, pc_incr, br_add_out,
dmem_rdata;
// control signals
wire RegWrite, Branch, PCSrc, RegDst, MemtoReg, MemRead,
MemWrite, ALUSrc, Zero;
wire [1:0] ALUOp;
wire [2:0] Operation;

## Slide 65: Single-Cycle Verilog - Part 3
// module instantiations
reg32 PC(clk, reset, pc_next, pc);
add32 PCADD(pc, 32'd4, pc_incr);
add32 BRADD(pc_incr, b_offset, b_tgt);
reg_file RFILE(clk, RegWrite, rs, rt, rfile_wn, rfile_rd1,
rfile_rd2, rfile_wd);
alu ALU(Operation, rfile_rd1, alu_b, alu_out, Zero);
rom32 IMEM(pc, instr);
mem32 DMEM(clk, MemRead, MemWrite, alu_out, rfile_rd2,
dmem_rdata);
and BR_AND(PCSrc, Branch, Zero);

## Slide 66: Single-Cycle Verilog - Part 4
mux2 #(5) RFMUX(RegDst, rt, rd, rfile_wn);
mux2 #(32) PCMUX(PCSrc, pc_incr, b_tgt, pc_next);
mux2 #(32) ALUMUX(ALUSrc, rfile_rd2, extend_immed, alu_b);
mux2 #(32) WRMUX(MemtoReg, alu_out, dmem_rdata, rfile_wd);
control_single CTL(.opcode(opcode), .RegDst(RegDst),
.ALUSrc(ALUSrc), .MemtoReg(MemtoReg),
.RegWrite(RegWrite), .MemRead(MemRead),
.MemWrite(MemWrite), .Branch(Branch),
.ALUOp(ALUOp));
alu_ctl ALUCTL(ALUOp, funct, Operation);
endmodule

## Slide 67: Project 2 - Extending the SC MIPS Model
Download files from Website
Simulate to gain familiarity with operation
Modify the design to support:
  addi rd, rs, rt
  bne rs, rt (in addition to beq)
  j addr
Modify ROM to contain a test program
  Write short assembly language to test all instructions
  Include a loop that executes at least 4 times
  Modify ROM code

## Slide 68: Demo: Simulating mips_single
ROM Contains the following program
  lw $2, 4($0) # r2=1
  lw $3, 8($0) # r3=2
  lw $4, 20($0) # r4=5
  add $5, $0, $0 # r5=0
  add $5, $5, $1 # r5 = r5 + 1
  slt $6, $4, $5 # is $5 >= r4?
  beq $6, $zero, -3 # if not, go back 2
  sw $6, 0($zero) # MEM[0] = $5
Connections to watch:
  PC, Instruction
  Instruction fields: opcode, rs, rt, rd, immed, etc.
  Register file: rfile_wn, regfile_rd1, regfile_rd2
  ALU: alu_b, alu_out, Zero

## Slide 69: Demo: Simulating mips_single